Monthly means of daily mean temperature

ERA-Interim : 6-hourly synoptic data

For each grid cell :
- Temperture lapse rates for pressure levels from 1000 to 3000 h Pa	Г
- with linear regression
Between grid cells :
- Interpolation of temperature to sea level	t0
- using the derived lapse rates
Between grid cells :
- Interpolation of mean monthly temperature	t = t0 + Г * elev
- with B-spline interpolation
- and projection on the elevational surface of the DEM	elev (GMTED2010 30 arc sec)

Maximum and minimum temperatures

ERA-interim : 3-hourly data of min/max temp since previous post processing data field

- Interpolation of min and max temperatures (30 arc sec) from t
- with B-spline interpolation
- Respective differences between min and max temperatures ∆t_era_min / ∆t_era_max
- .	t_min = t + ∆t_era_min
  t_max = t + ∆t_era_max

Wind effect correction

ERA-interim : u-wind and v-wind components (10 m level)

- Interpolation to CHELSA grid resolution
- with B-spline interpolation
- Projection to a world Mercator projection
- and combined to a directional grid

For each grid cell :
- Windward and leeward components	HW / HL
- Final wind-effect parameter	H = HL * HW (between 0.7 and 1.3)

Valley exposition correction

For each grid cell :
- Windward and leeward components	HW / HL
- with linear search distance of 300km in steps of 5° from 0° to 355°
- Scale of HL towards higher elevations	E = HL ^ (elev / c)
- with constant c = 9000 m

Boundary layer correction

ERA-interim :

- Obtention of boundary layer height	B = Bera + elev + f
  (height of the monthly means of daily mean boundary layer Bera)
- with B-spline interpolation
- with constant f = 500 m

For each grid cell :
Distance between a grid cell and B	d = elev - B

Maximum distance between B and all grid cells falling	dmax
within a respective 0.75° grid cell

Proportional distribution of H to all grid cells falling	HWB / HLB
within a respective 0.75° grid cell

Monthly precipitation sums

ERA-interim : monthly means of daily forecast accumulations of total precipitation	Pera

monthly means at time 0:00, step 12 and time 12:00, step 12 * number of days in the month

Monthly bias correction

GPCC : monthly precipitation values Pgpcc

- Monthly bias	Rm = Pgpcc / Pera
- caused by ERA-interim parameterization
- and excessive / insufficient precipitation of forecast algorithm for each month (1979-2013)

- Interpolation of gaps in Rm grid
- with multilevel B-spline interpolation with 14 errors levels to a 0.75° resolution
- to obtain of gap-free grid surface
- Correction of monthly precipitation sums	Pm = Pera * Rm
- to obtain gap-free with gap-free bias correction surface Rm

Monthly precipitation including orographic effects

- Distribution of monthly precipitation sums	P
- with linear relationship	P = (H / Ĥ) * Pm
- with Ĥ the mean win effect

Station bias correction

GHCN, MeteoSwiss, DWD : precipitation from a set of meteorological station Pstation

Bias ratio	Pstation / P

- Interpolation of bias ratio
- with multilevel B-spline interpolation with 14 errors levels to a 0.1° resolution
- to obtain of gap-free grid surface

Correction of monthly precipitation sums	P = P * Bias ratio

Climatologies

mean monthly sum of precipitation in the years 1979-2013 for each month

For each grid cell with station(s) :
- Bias between annual accumulations and GPCC climatology
- Interpolation of bias ratio
- with multilevel B-spline interpolation to a 0.25° resolution

Obtention of final climatologies = mean annual precipitation sums * Bias ratio

Bioclimatic parameters